## Slide 1: ATE 252 Introduction to Electricity
Instructor:
Patricia Thompson

## Slide 2: Electricity
What is it?
  Movement of electrons
Brief history
  2750 bc – Greeks
  1600 ad – Gilbert defined static electricity
    elektron, the Greek word for "amber”

## Slide 3: Electricity
History
  1800’s
    Alessandro Volta
    André-Marie Ampère
    Michael Faraday
    Thomas Edison
    Nikola Tesla
    Many other inventors

## Slide 4: Electricity
Atom
  Proton
    Positive charge
    Small and dense
  Neutron
    No charge
    Along with protons, make up the nucleus
  Electron

## Slide 5: Electricity
Electron
  Negative charge
  Large and light
  Float around the nucleus
  Valence electrons
    Electrons furthest away from nucleus
    Maximum of eight valence electrons

## Slide 6: Electricity
Conductors
  One or two valence electrons
  Aluminum, gold, copper, silver
Insulators
  Seven or eight valence electrons
  Wood, glass, rubber, plastic
Semiconductors
  Four valence electrons
  Silicon

## Slide 7: Electricity
Two types of current
  Direct current (DC)
    Electrons continuously move in one direction
    Batteries, DC power supplies
    Have a positive and a negative

## Slide 8: Electricity
Two types of current
  Alternating current (AC)
    Electrons move together but change directions

## Slide 9: Schematic
Standard method of drawing electrical circuits
  Shows what components are in the circuit
  How the components are connected to each other
  Helps to organize for installation and troubleshooting

## Slide 10: Schematics
Actual
Schematic

## Slide 11: Circuit
Complete circuit
  Must have
    At least one continuous path
    Power source
    Load
    Conductor
    Insulator

## Slide 12: Circuit
Usually will also have
  Control device
    Switch
  Protective device
    Fuse

## Slide 13: Four Quantities
Voltage
  Force that starts electrons moving
  Also known as Electromotive Force (EMF)
    Abbreviation: V (or E)
    Unit: Volt (V), named for Alessandra Volta
    Measured in parallel
    Schematic symbol:
      DC AC

## Slide 14: Four Quantities
Current
  Rate the electrons flow
    Abbreviation: I
    Unit: Ampere (Amp or A)
      Usually in mA, 1 mA=0.001A
    Measured:
      DMM: in series
      Clampmeter: clamp wire
    Schematic Symbol:

## Slide 15: Four Quantities
Resistance
  Opposed the flow of electrons
    Abbreviation: R
    Unit: Ohm (Ω)
      Could be kΩ, 1 kΩ = 1000 Ω
    Measured in parallel with at least one end disconnected from circuit
    Schematic symbol:

## Slide 16: Four Quantities
Power
  Rate energy is converted
    Abbreviation: P
    Unit: Watt (W) after James Watt
      Charged by kWhr, 1kW = 1000W
    Measured with a wattmeter or calculated value
    Schematic symbol: Not shown

## Slide 17: Four Quantities
Related to each other by
  Ohm’s Law
    Relationship between voltage, current, and resistance (V, I, and R).
    V = IR

## Slide 18: Circuits
Series
Parallel
Combination (Series and parallel)

## Slide 19: Series Circuits
Components are connected end to end
Only one path for current flow

## Slide 20: Series Circuits
Advantage
  Distribute voltage across many devices
  Lower power consumption so lower cost
Disadvantage
  If one component goes bad, all components will turn off

## Slide 21: Parallel Circuits
Two or more paths for current to flow
Components positive and negative terminal s are connected to each other

## Slide 22: Parallel Circuits
Advantage
  If one component is off, others will remain on
  Control of current flow
Disadvantage
  Higher power consumption so higher cost

## Slide 23: Analog vs digital
Analog signals have a range of values
0V
0.5 V
0.75 V
1.0 V

## Slide 24: Analog vs digital
Digital signals have two discrete values
0 V
0 V
5 V
5 V

## Slide 25: Analog vs digital
Analog devices

## Slide 26: Analog vs digital
Digital devices

## Slide 27: Digital signals
Digital signals can be compared to a light switch, it is either on or off
On may be referred to as Off may be referred to as
  High • low
  Logic 1 • Logic 0
  On • off

## Slide 28: Logic gates
Seven basic gates
  AND
  OR
  NOT
  NAND
  NOR
  Exclusive OR (XOR)
  Exclusive NOR (XNOR)

## Slide 29: AND gate
Schematic
Truth table
Mathematical expression
  A X B = A
Common ic chip
  7408 chip
  Contains 4 gates
  Pin 7: gnd
  Pin 14: vcc = +5 V
  pins 1 & 2, 4 & 5, 9 & 10, and 12 & 13: inputs
  Pins 3, 6, 8, and 11: outputs
A | B | Q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 30: OR gate
Schematic
Truth table
Mathematical expression
  A + B = Q
Common ic chip
  7432 chip
  Contains 4 gates
  Pin 7: gnd
  Pin 14: vcc = +5 V
  pins 1 & 2, 4 & 5, 9 & 10, and 12 & 13: inputs
  Pins 3, 6, 8, and 11: outputs
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 31: NOT gate
inverter
Schematic
Truth table
Mathematical expression
Common ic chip
  7404 chip
  Contains 6 gates
  Pin 7: gnd
  Pin 14: vcc = +5 V
  pins 1, 3, 5, 9, 11, and 13: inputs
  Pins 2, 4, 6, 8, 10, and 12: outputs
A | Q
0 | 1
1 | 0

## Slide 32: NAnd “not and” gate
Schematic
Truth table
Mathematical expression
Common ic chip
  7400 chip
  Contains 4 gates
  Pin 7: gnd
  Pin 14: vcc = +5 V
  pins 1 & 2, 4 & 5, 9 & 10, and 12 & 13: inputs
  Pins 3, 6, 8, and 11: outputs
A | B | Q
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Q

## Slide 33: Nor “Not or” gate
Schematic
Truth table
Mathematical expression
Common ic chip
  7402 chip
  Contains 4 gates
  Pin 7: gnd
  Pin 14: vcc = +5 V
  pins 2 & 3, 5 & 6, 8 & 9, and 11&12: inputs
  Pins 1, 4, 10, and 13: outputs
A | B | Q
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 34: Xor “exclusive or” gate
Schematic
Truth table
Mathematical expression
Common ic chip
  7486 chip
  Contains 4 gates
  Pin 7: gnd
  Pin 14: vcc = +5 V
  pins 1 & 2, 4 & 5, 9 & 10, and 12 & 13: inputs
  Pins 3, 7, 8, and 11: outputs
A | B | Q
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 35: xNor “exclusive nor” gate
Schematic
Truth table
Mathematical expression
Common ic chip
  74266 chip
  Contains 4 gates
  Pin 7: gnd
  Pin 14: vcc = +5 V
  pins 1 & 2, 5 & 6, 8 & 9, and 12 & 13: inputs
  Pins 3, 4, 10, and 11: outputs
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1